## Slide 1: Q-Learning Based Dynamic Done Trajectory Planning in Uncertain Environments
Subrahmanya Chandra Bhamidipati, Prasad Calyam

## Slide 2: Revolutionizing Last-Mile Delivery
Problem:
  Drones face connectivity and navigation challenges in dynamic environments.
Objective:
  Introduce Q-learning-based model to enable drones to adapt to network disruptions.
  Ensure safety and efficient delivery even without continuous communication with ground control.
Drones increasingly used in logistics, urban deliveries, disaster relief.

## Slide 3: Navigating Challenges
Core Challenges:
  Unstable Network Connectivity: Network congestion, obstacles, or distance cause communication loss.
  Dynamic Environments: Require drones to navigate around obstacles like buildings, trees, or traffic congestion zones.
Goal: Enable drones to independently make safe, real-time decisions during network disruptions.

## Slide 4: Q-Learning for Intelligent Drone Decisions
Model Structure:
  State Space: Drone’s position, obstacles, network status, battery level, in congestion, nearest congestion.
  Action Space: Movement in eight directions; accelerate/decelerate.
Reward Structure:
  Positive Rewards: Delivery, reaching Depot, Emergency Landing Spot
  Negative Rewards: Battery depletion, congestion entry, collisions.
State
Action
Reward
Next
State

## Slide 5: Testing in Simulations
Assumptions
  Single Drone
Simulation Environment:
  Grid Setup: 800x800 pixel environment
  Grid Elements: Start/end positions, emergency landing spots, depot, dynamic congestion zones.
Simulation Parameters:
  Episodes: 100,000 for training.
800 px
800 px
Emergency Landing Spot
Depot
Customer
Obstacle
Cong.
Zone

## Slide 6: Scenario Analysis
Scenario 1: After delivery, drone decides to land at an emergency site.

## Slide 7: Scenario Analysis
  Scenario 2: Drone returns to depot if delivery becomes too risky

## Slide 8: Results
Performance Analysis:
  Reward Comparison: Q-learning shows 23% higher reward accumulation than A*. (A* algorithm goes for the customer and then to the emergency landing spot always)

## Slide 9: Improvements since paper
Introduction of multi drone system with multiple customers

## Slide 10: Discussion
Key Insights:
  Safety: Prioritizes safe recovery and avoids high-risk situations
  Energy Efficiency: Balances successful deliveries with energy conservation for longer missions.
  Flexibility: Enables real-time adaptation without continuous supervision.
Limitations:
  Higher computational load with expanding environment complexity.
Future Work:
  Advanced RL algorithms like DQN, PPO
  Real-world testing to validate model.